## Slide 1: BSE-18T State Machine Validation

## Slide 2: State Machine

## Slide 3: INTRODUCTION
The Sensors with ID’s as shown below are updated with the new BSE18T HDS8_OTA_V07.0A_20250904.gbl firmware
  78:1C:9D:7C:48:81
  FC:4D:6A:E3:B7:0C
The following tests are performed on the Sensors
  Standby to Normal to Standby
  Normal to Delta P to Normal
  Normal to Monitoring to Normal
  Monitoring to Delta P to Monitoring

## Slide 4: TEST SETUP

## Slide 5: STANDBY to NORMAL to STANDBY(B7:0C)
Time | Pressure Applied | Mode | No of Packets ch 37 | No of Packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
10:00 AM | 0 PSI | STANDBY |  |  |  |  | 
10:09 AM | 10 PSI |  |  |  |  |  | 
10:10 AM | 10 PSI | Normal | 3 | 3 | 0 | 9.42 PSI | 0
10:15 AM | 10 PSI | Normal | 1 | 4 | 1 | 9.42 PSI | 5 min
10:20 AM | 0 PSI |  |  |  |  |  | 
10:20 AM | 0 PSI | Normal | 4 | 4 | 1 | 0 PSI | 5 min
10:25 AM | 0 PSI | Normal | 2 | 4 | 0 | 0 PSI | 5 min
10:30 AM | 0 PSI |  |  |  |  |  | 
No TX from the Sensor
Changed pressure from 0 PSI to 10 PSI
Changed pressure from 10 PSI to 0 PSI
No TX from the Sensor (Should I expect one more Normal Mode Tx?)

## Slide 6: STANDBY to NORMAL to STANDBY(B7:0C)

## Slide 7: STANDBY to NORMAL to STANDBY(B7:0C)
5 min
Only lasted in Normal Mode for 5 mins at 0 PSI

## Slide 8: STANDBY to NORMAL to STANDBY(48:81)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
10:00 AM | 0 PSI | STANDBY |  |  |  |  | 
10:09 AM | 10 PSI |  |  |  |  |  | 
10:09 AM | 10 PSI | NORMAL | 2 | 2 | 2 | 9.78 PSI | 0
10:14 AM | 10 PSI | NORMAL | 3 | 3 | 2 | 9.42 PSI | 5 min
10:19 AM | 10 PSI | NORMAL | 2 | 2 | 1 | 9.42 PSI | 5 min
10:20 AM | 0 PSI |  |  |  |  |  | 
10:24 AM | 0 PSI | NORMAL | 4 | 2 | 0 | 0 PSI | 5 min
10:29 AM | 0 PSI |  |  |  |  |  | 
No TX from the Sensor
Changed pressure from 0 PSI to 10 PSI
Changed pressure from 10 PSI to 0 PSI
No TX from the Sensor (Should I expect one more Normal Mode Tx?)

## Slide 9: STANDBY to NORMAL to STANDBY(48:81)

## Slide 10: STANDBY to NORMAL to STANDBY(48:81)

## Slide 11: Conclusion
Standby Mode
  The Sensor does not transmit any advertisements during Standby Mode for both the Sensors
Standby to Normal Mode(Δ P ≥ 4PSI) 
  When the pressure was increased from 0 PSI to 10 PSI both the Sensors go into Normal Mode
  The Normal Mode advertisements are transmitted every 5 mins
Normal to Standby Mode(P<3 PSI for 10 mins) -?
  Sensor B7:0C- At 10:30 AM, do we expect the Sensor to transmit one more normal mode adv?)
  Sensor 48:81- At 10:29 AM, do we expect the Sensor to transmit one more normal mode adv?)

## Slide 12: Normal to Delta P to Normal(B7:0C)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
11:28 AM | 10 PSI | NORMAL | 3 | 1 | 0 | 9.42 PSI | 0
11:29 AM | 50 PSI |  |  |  |  |  | 
11:30 AM | 50 PSI | DELTA P | 9 | 9 | 9 | 50.03 PSI | 1 min
11:33 AM | 50 PSI | NORMAL | 4 | 6 | 1 | 50.03 PSI | 3 min
11:38 AM | 50 PSI | NORMAL | 1 | 3 | 0 | 50.03 PSI | 5 min
11:38 AM | 10 PSI |  |  |  |  |  | 
11:39 AM | 10 PSI | DELTA P | 10 | 11 | 9 | 9.42 PSI | 1 min
11:43 AM | 10 PSI | NORMAL | 3 | 4 | 4 | 9.42 PSI | 4 min
11:48 AM | 10 PSI | NORMAL | 3 | 2 | 2 | 9.42 PSI | 5 min
Increased Pressure from 10 PSI to 50 PSI
Decreased Pressure from 10 PSI to 50 PSI
Delta P 5 secs
Delta P 5 secs

## Slide 13: Normal to Delta P to Normal(B7:0C)

## Slide 14: Normal to Delta P to Normal(B7:0C)
3 min
4 min

## Slide 15: Normal to Delta P to Normal(48:81)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
11:29 AM | 10 PSI | NORMAL | 2 | 3 | 1 | 9.42 PSI | 0
11:29 AM | 50 PSI |  |  |  |  |  | 
11:30 AM | 50 PSI | DELTA P | 12 | 7 | 9 | 50.03 PSI | 1 min
11:34 AM | 50 PSI | NORMAL | 2 | 3 | 1 | 50.03 PSI | 4 min
11:38 AM | 10 PSI |  |  |  |  |  | 
11:39 AM | 10 PSI | DELTA P | 9 | 7 | 7 | 9.42 PSI | 1 min
11:39 AM | 10 PSI | NORMAL | 2 | 2 | 2 | 9.42 PSI | 
11:44 AM | 10 PSI | NORMAL | 1 | 3 | 2 | 9.42 PSI | 5 min
11:49 AM | 10 PSI | NORMAL | 2 | 3 | 0 | 9.42 PSI | 5 min
Increased Pressure from 10 PSI to 50 PSI
Decreased Pressure from 50 PSI to 10 PSI
Delta P 5 secs
Delta P 5 secs

## Slide 16: Normal to Delta P to Normal(48:81)

## Slide 17: Conclusion
Normal Mode
  Both the Sensors advertised every 5 mins in Normal Mode as per the State Machine
Delta P Mode(ΔP ≥ 30 PSI)
  Both the Sensors entered Delta P Mode when the pressure was increased from 10 PSI to 50 PSI.
  The Delta P time observed for both the Sensors was 5 seconds in total
Delta P Mode to Normal Mode
  Both the Sensors exited from Delta P Mode back to Normal Mode as per the State Machine

## Slide 18: Normal to Monitoring to Normal(B7:0C)
Condition Tested-
  Normal to Monitoring(P≥80 PSI)
  Monitoring to Normal(P<60 PSI)
Time | Pressure Applied | Mode | No of Packets ch 37 | No of Packets ch 38 | No of Packets ch 39 | Pressure on BLE | Time Delta
7:52 AM | 70 PSI | NORMAL | 4 | 3 | 1 | 70.34 PSI | 3 min
7:57 AM | 70 PSI | NORMAL | 2 | 2 | 1 | 70.34 PSI | 5 min
7:57 AM | 85 PSI |  |  |  |  |  | 
7:58 AM | 85 PSI | MONITORING | 3 | 5 | 3 | 84.84 PSI | 1 min
8:23 AM | 85 PSI | MONITORING | 3 | 2 | 1 | 84.84 PSI | 25 min
8:49 AM | 85 PSI | MONITORING | 1 | 2 | 1 | 84.84 PSI | 25 min
Increased pressure from 70 PSI to 85 PSI

## Slide 19: Normal to Monitoring to Normal(B7:0C)
Time | Pressure Applied | Mode | No of Packets ch 37 | No of Packets ch 38 | No of Packets ch 39 | Pressure on BLE | Time Delta
9:14 AM | 85 PSI | MONITORING | 3 | 4 | 2 | 84.84 PSI | 25 min
9:17 AM | 50 PSI |  |  |  |  |  | 
9:18 AM | 50 PSI | NORMAL | 3 | 5 | 1 | 50.03 PSI | 4 min
9:23 AM | 50 PSI | NORMAL | 3 | 4 | 1 | 50.03 PSI | 5 min
Decreased pressure from 85 PSI to 50 PSI

## Slide 20: Normal to Monitoring to Normal(B7:0C)
Normal to Monitoring

## Slide 21: Normal to Monitoring to Normal(B7:0C)

## Slide 22: Normal to Monitoring to Normal(48:81)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
7:52 AM | 70 PSI | NORMAL | 1 | 2 | 1 | 70.34 PSI | 0
7:57 AM | 70 PSI | NORMAL | 0 | 2 | 2 | 70.34 PSI | 5 min
7:57 AM | 85 PSI |  |  |  |  |  | 
7: 58 AM | 85 PSI | MONITORING | 2 | 2 | 2 | 84.84 PSI | 1 min
8:24 AM | 85 PSI | MONITORING | 4 | 2 | 4 | 84.84 PSI | 25 min
8:49 AM | 85 PSI | MONITORING | 1 | 2 | 3 | 84.84 PSI | 25 min
9:15 AM | 85 PSI | MONITORING | 2 | 1 | 2 | 84.84 PSI | 25 min
9:17 AM | 50 PSI |  |  |  |  |  | 
9:18 AM | 50 PSI | NORMAL | 4 | 4 | 3 | 50.03 PSI | 1 min
9:23 AM | 50 PSI | NORMAL | 2 | 3 | 1 | 50.03 PSI | 5 min
Increased pressure from 70 to 85 PSI
Decreased pressure from 85 PSI to 50 PSI

## Slide 23: Normal to Monitoring to Normal(48:81)
Normal to Monitoring

## Slide 24: Normal to Monitoring to Normal(48:81)

## Slide 25: Conclusion
Normal Mode
  Both the Sensors advertised every 5 mins in Normal Mode as per the State Machine
Normal to Monitoring Mode(P≥80 PSI) 
  Both the Sensors enter Monitoring Mode from Normal Mode when the Pressure applied to the Sensors is increased beyond 80 PSI
  Both the Sensors transmitted every 25 mins in Monitoring Mode as per the State Machine
Monitoring Mode to Normal Mode(P<60 PSI) 
  Both the Sensors returned to Normal Mode from Monitoring Mode when the Pressure Applied was less than 60 PSI

## Slide 26: Normal to Monitoring to Normal(B7:0C)
Condition Tested
  Normal to Monitoring(ΔP<5 PSI for 15 mins)
  Monitoring to Normal(ΔP>4.5 PSI for 15 mins)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
1:09 PM | 50 PSI |  |  |  |  |  | 
1:10 PM | 50 PSI | NORMAL | 1 | 5 | 1 | 50.03 PSI | 0
1:15 PM | 50 PSI | NORMAL | 1 | 3 | 1 | 50.03 PSI | 5 min
1:20 PM | 50 PSI | NORMAL | 1 | 3 | 0 | 50.03 PSI | 5 min
1:20 PM | 51 PSI |  |  |  |  |  | 
1:21 PM | 52 PSI |  |  |  |  |  | 
1:22 PM | 53 PSI |  |  |  |  |  | 
Increased pressure from 0(Standby) to 50 PSI
Increased pressure from 50 to 51 PSI
Increased pressure from 51 to 52 PSI
Increased pressure from 52 to 53 PSI

## Slide 27: Normal to Monitoring to Normal(B7:0C)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
1:23 PM | 54 PSI |  |  |  |  |  | 
1:25 PM | 54 PSI | NORMAL | 4 | 4 | 4 | 53.66 PSI | 5 min
1:26 PM | 54 PSI | MONITORING | 1 | 3 | 1 | 53.66 PSI | 1 min
1:27 PM | 54 PSI | NORMAL | 1 | 1 | 1 | 53.66 PSI | 1 min
1:32 PM | 54 PSI | NORMAL | 2 | 2 | 1 | 53.66 PSI | 5 min
1:37 PM | 54 PSI | NORMAL | 3 | 4 | 1 | 53.66 PSI | 5 min
Increased pressure from 53 to 54 PSI

## Slide 28: Normal to Monitoring to Normal(B7:0C)

## Slide 29: Normal to Monitoring to Normal(B7:0C)

## Slide 30: Normal to Monitoring to Normal(48:81)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
1:09 PM | 50 PSI |  |  |  |  |  | 
1:09 PM | 50 PSI | NORMAL | 5 | 2 | 1 | 50.03 PSI | 0
1:14 PM | 50 PSI | NORMAL | 3 | 3 | 1 | 50.03 PSI | 5 min
1:19 PM | 50 PSI | NORMAL | 3 | 3 | 1 | 50.03 PSI | 5 min
1:20 PM | 51 PSI |  |  |  |  |  | 
1:21 PM | 52 PSI |  |  |  |  |  | 
1:22 PM | 53 PSI |  |  |  |  |  | 
1:23 PM | 54 PSI |  |  |  |  |  | 
1:25 PM | 54 PSI | NORMAL | 3 | 2 | 3 | 53.66 PSI | 5 min
Increased pressure from 0(Standby) to 50 PSI
Increased pressure from 50 to 51 PSI
Increased pressure from 51 to 52 PSI
Increased pressure from 52 to 53 PSI
Increased pressure from 53 to 54 PSI

## Slide 31: Normal to Monitoring to Normal(48:81)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
1:26 PM | 54 PSI | MONITORING | 0 | 0 | 3 | 53.29 PSI | 1 min
1:27 PM | 54 PSI | NORMAL | 4 | 1 | 1 | 53.66 PSI | 1 min
1:32 PM | 54 PSI | NORMAL | 3 | 2 | 3 | 53.29 PSI | 5 min
1:37 PM | 54 PSI | NORMAL | 0 | 1 | 1 | 53.29 PSI | 5 min

## Slide 32: Normal to Monitoring to Normal(48:81)

## Slide 33: Normal to Monitoring to Normal(48:81)

## Slide 34: Conclusion
Normal Mode
  Both the Sensors advertised every 5 mins in Normal Mode as per the State Machine
Normal Mode to Monitoring Mode (ΔP<5 PSI for 15 mins) X
  Both the Sensors do not satisfy this condition
  Why did Sensor B7:0C enter Monitoring Mode at 1:26 PM and exit Monitoring Mode at 1:27 PM?
  Why did Sensor 48:81 enter Monitoring Mode at 1:26 PM and exit Monitoring Mode at 1:27 PM?

## Slide 35: Normal to Monitoring to Normal(B7:0C)- Repeat
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
10:39 AM | 54 PSI | NORMAL | 4 | 3 | 0 | 53.29 PSI | 0
10:44 AM | 57 PSI |  |  |  |  |  | 
10:44 AM | 57 PSI | NORMAL | 3 | 5 | 2 | 53.29 PSI | 5 min
10:49 AM | 57 PSI | NORMAL | 4 | 3 | 1 | 56.56 PSI | 5 min
10:54 AM | 57 PSI | MONITORING | 2 | 5 | 1 | 56.56 PSI | 5 min
10:55 PM | 57 PSI | NORMAL | 2 | 3 | 0 | 56.56 PSI | 1 min
11:00 PM | 57 PSI | NORMAL | 3 | 3 | 2 | 56.56 PSI | 5 min
11:05 PM | 57 PSI | NORMAL | 3 | 4 | 1 | 56.56 PSI | 5 min
11:10 PM | 57 PSI | MONITORING | 3 | 3 | 0 | 56.56 PSI | 5 min
11:11 PM | 57 PSI | NORMAL | 3 | 4 | 0 | 56.56 PSI | 1 min
Increase pressure from 54 PSI to 57 PSI

## Slide 36: Normal to Monitoring to Normal(B7:0C)- Repeat

## Slide 37: Normal to Monitoring to Normal(B7:0C)- Repeat

## Slide 38: Normal to Monitoring to Normal(48:81)- Repeat
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
10:39 AM | 54 PSI | NORMAL | 1 | 2 | 2 | 53.29 PSI | 0
10:44 AM | 57 PSI |  |  |  |  |  | 
10:44 AM | 57 PSI | NORMAL | 4 | 2 | 0 | 56.56 PSI | 5 min
10:49 AM | 57 PSI | NORMAL | 3 | 4 | 2 | 56.56 PSI | 5 min
10:55 AM | 57 PSI | MONITORING | 1 | 1 | 1 | 56.56 PSI | 5 min
10:56 AM | 57 PSI | NORMAL | 1 | 2 | 2 | 56.56 PSI | 1 min
11:01 AM | 57 PSI | NORMAL | 3 | 2 | 0 | 56.56 PSI | 5 min
11:06 AM | 57 PSI | NORMAL | 2 | 3 | 1 | 56.56 PSI | 5 min
11:11 AM | 57 PSI | MONITORING | 2 | 3 | 1 | 56.56 PSI | 5 min
11:12 AM | 57 PSI | NORMAL | 3 | 3 | 2 | 56.56 PSI | 1 min
Increase pressure from 54 PSI to 57 PSI

## Slide 39: Normal to Monitoring to Normal(48:81)- Repeat

## Slide 40: Normal to Monitoring to Normal(48:81)- Repeat

## Slide 41: Conclusion
Normal Mode
  Both the Sensors advertised every 5 mins in Normal Mode as per the State Machine
Normal Mode to Monitoring Mode (ΔP<5 PSI for 15 mins) X
  Both the Sensors do not satisfy this condition
  Why did the Sensor B7:0C enter Monitoring Mode at 10:54 AM? And 11:10 AM?
  Why did the Sensor 48:81 enter Monitoring Mode at 10:55 AM? and 11:11 AM?

## Slide 42: Monitoring to Delta P to Monitoring(B7:0C)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
8:53 AM | 85 PSI | MONITORING | 3 | 4 | 1 | 84.48 PSI | 0
9:18 AM | 85 PSI | MONITORING | 0 | 1 | 0 | 84.48 PSI | 25 min
9:22 AM | 120 PSI |  |  |  |  |  | 
9:22 AM | 120 PSI | DELTA P | 13 | 6 | 9 | 119.65 PSI | 4 min
9:37 AM | 120 PSI | NORMAL | 3 | 3 | 4 | 119.65 PSI | 15 min
9:38 AM | 120 PSI | MONITORING | 3 | 3 | 4 | 119.65 PSI | 1 min
Increased pressure from 85 PSI to 120 PSI
Expected Monitoring Mode at 9:43

## Slide 43: Monitoring to Delta P to Monitoring(B7:0C)

## Slide 44: Monitoring to Delta P to Monitoring(B7:0C)

## Slide 45: Monitoring to Delta P to Monitoring(48:81)
Time | Pressure Applied | Mode | No of packets ch 37 | No of packets ch 38 | No of packets ch 39 | Pressure on BLE | Time Delta
8:54 AM | 85 PSI | MONITORING | 1 | 4 | 0 | 84.48 PSI | 0
9:19 AM | 85 PSI | MONITORING | 1 | 2 | 1 | 84.48 PSI | 25 min
9:22 AM | 120 PSI |  |  |  |  |  | 
9:22 AM | 120 PSI | DELTA P | 13 | 8 | 7 | 119.65 PSI | 3 min
9:36 AM | 120 PSI | NORMAL | 2 | 1 | 3 | 119.65 PSI | 14 min
9:37 AM | 120 PSI | MONITORING | 2 | 2 | 2 | 119.65 PSI | 1 min
Increase pressure from 85 PSI to 120 PSI
Expected Monitoring Mode at 9:44 AM

## Slide 46: Monitoring to Delta P to Monitoring(48:81)

## Slide 47: Monitoring to Delta P to Monitoring(48:81)

## Slide 48: Conclusion
Monitoring Mode X
  Why did the Sensor B7:0C transmit Monitoring Mode packets at 9:38 AM instead of 9:43 AM?
  Why did the Sensor 48:81 transmit Monitoring Mode packets at 9:37 AM instead of 9:44 AM?
Monitoring Mode to Delta P Mode 
  Both the Sensors enter Delta P Mode when a ΔP>=30 PSI is applied while in Monitoring Mode
Delta P Mode to Monitoring Mode X
  Why did the Sensor B7:0C first enter Normal Mode at 9:37 AM before returning to Monitoring Mode at 9:38 AM?
  Why did the Sensor 48:81 enter Normal Mode at 9:36 AM before returning to Monitoring Mode at 9:37 AM?